## Slide 1
RADIATION ONCOLOGY · UCT / GSH REGISTRAR TRAINING · 2026
What Makes a Plan Good?
3DCRT Plan Evaluation Workshop — Theory & Practical Module
Tamerone Manasse
UCT / GSH Registrars · 2026
1

## Slide 2
HOW THIS SESSION RUNS
2 Hours · 5 Cases · One framework.
0:00
Theory — framework, DVH, OARs, red flags
18 min
0:18
Case 1: Breast — full scorecard exercise
22 min
0:40
Case 2: Gynaecology — trade-off
10 min
0:50
Case 3: Prostate — trade-off
10 min
1:00
Case 4: Pituitary — coplanar vs non-coplanar
10 min
1:10
Case 5: H&N — 4-field vs 3-field
10 min
1:20
Buffer / questions / overflow
30 min
1:50
Wrap-up + key takeaways
10 min
By the end you can: Apply FCB-CHOPS · Read a DVH · Explain CI & HI · Apply OAR constraints · Triage a plan
2

## Slide 3
THE FOUNDATION
A good plan answers four questions — in order.
01
Does it treat the target?
Adequate dose throughout the target — no geographic miss, no cold spot where tumour lives.
02
Does it spare normal tissue?
Every OAR within tolerance — judged against the right dose-volume metric for that organ's architecture.
03
Is it technically sound?
Sensible isocentre, beam geometry, weighting — the plan is intentionally built, not just generated.
04
Is it deliverable & robust?
Achievable on the machine, stable to setup and anatomy variation.
"A plan is never perfect — it is the best defensible compromise."
3

## Slide 4
THE REALITY OF PLAN EVALUATION
Bad, acceptable, trade-off — or good?
CLEARLY BAD
Unsafe or unacceptable. Easy to spot, easy to reject. Geographic miss, serial OAR breach, undeliverable MU.
ACCEPTABLE
Passes all constraints — but a better plan is clearly achievable with reasonable effort. Not wrong, but not optimal.
TRADE-OFF
Competing priorities pull against each other. Fixing one worsens another. Needs clinical judgement and documentation.
GOOD
Balanced, robust, clinically appropriate. Target covered, OARs spared, technically sound, documented.
THE GUT-CHECK: "Would I confidently treat my own family member with this plan?" — if no, name exactly what would have to change.
4

## Slide 5
THE FRAMEWORK — ORIGINS AND EVOLUTION
2017 — ORIGINAL
CB-CHOP
Jimenez et al. · Pract Radiat Oncol 2017
C
Contours
B
Beam Arrangement
C
Coverage
H
Heterogeneity / Hotspots
O
Organs at Risk
P
Prescription
→
+F +S
2024 — EVOLUTION
FCB-CHOPS
Weisman et al. · Adv Radiat Oncol 2024 · PMID 40017913
F
Fusion / Imaging
NEW
C
Contours
B
Beam Arrangement
C
Coverage
H
Heterogeneity / Hotspots
O
Organs at Risk
P
Prescription
S
Summation
NEW
5

## Slide 6
A SYSTEMATIC FRAMEWORK
FCB-CHOPS — eight checkpoints, every plan
F
Fusion / Imaging
Verify image fusion accuracy — correct target & OAR anatomy
C
Contours
All target & OAR contours complete and anatomically correct
B
Beam Arrangement
Beam geometry and entry points appropriate for the target
C
Coverage
Prescribed dose adequately covers the target volume
H
Heterogeneity/Hotspots
Internal dose variation — acceptable high and low dose regions
O
Organs at Risk
OAR doses respect clinical constraints for each organ
P
Prescription
Correct dose, fractionation, normalisation, laterality documented
S
Summation
Cumulative dose from all courses — or explicitly acknowledge none
Start with Prescription. It defines treatment intent — confirm it before anything else.
The letters are a safety net, not a script. Work in whatever order the plan demands.
6

## Slide 7
01
BLOCK ONE
B
Beams & Technical Quality
⏱ 12 MINUTES
● Isocentre placement — position and tissue type
● Beam geometry, entry angles and arrangement
● MLC shaping, collimation and flash
● Wedges, field-in-field and dose shaping tools
● MU sanity check
3DCRT Plan Evaluation · Theory Module
7

## Slide 8
BLOCK B · BEAM ARRANGEMENT
Every beam should reach the target by the most direct, safest route
UNAVOIDABLE
ACCEPTABLE
4-field box — beams transit OARs
Whole pelvis, bilateral treatment — OAR transit is geometry-driven. Document field weighting; manage with DVH.
AVOIDABLE
RE-ANGLE
Beam transits OAR before reaching PTV
Left lateral must pass through OAR en route to PTV. This is avoidable — enter from the contralateral side.
SOLUTION
IPSILATERAL
Enter from the OAR-free side
AP + ipsilateral lateral — OAR on the contralateral side receives no direct beam dose.
Before accepting any OAR transit — ask: is there a beam arrangement that avoids it? If yes, use it. If no, document why.
8

## Slide 9
BLOCK B · TECHNICAL QUALITY
Technical red flags
Technical quality check
RISK
Isocentre in lung, air, or density interface — dose calculations unreliable
RISK
Beam transiting directly through a critical serial OAR — re-angle if any workable alternative exists
RISK
Hot spot outside the PTV — in skin, bowel, or OAR it is unacceptable regardless of magnitude
MAJOR
MLC clipped tight to PTV edge — no penumbra margin means a cold rim on every beam
MAJOR
Normalisation point in unstable tissue — lung, air, interface — every DVH number unreliable
✓ Isocentre — centred in PTV; not in lung or density interface
✓ Beam weighting — re-weight to pull hot spot into target
✓ Wedges — tilt isodoses to compensate for sloping surface
✓ Field-in-field (FiF) — sub-segments block emerging hot spots; routine in breast
✓ Monitor units — sanity check; excess MU adds scatter to whole patient
9

## Slide 10
BLOCK B · TECHNICAL QUALITY
Hot spots, dose gradient & integral dose
▶ Hot spot — location, not just size.
A 107% inside the PTV is fine; the same 107% in skin or an OAR is not. Location governs acceptability.
▶ Dose gradient
Dose should fall steeply between the PTV edge and any adjacent OAR. Check isodose slices for every beam entry.
▶ Integral dose / MU
Sanity-check the monitor units. Excess MU adds scatter and integral dose to the whole patient.
Don't just ask HOW BIG — ask WHERE it sits
Hot spot INSIDE the PTV — acceptable
107% inside the target is expected in 3DCRT. The prescription point is normalised to ~100%; a modest hotspot in the tumour itself is clinically acceptable. Monitor: ensure D2% < 107%
Hot spot OUTSIDE the PTV — concern
In OAR or skin = PROBLEM regardless of magnitude. Causes: deep isocentre, unweighted beams, density heterogeneity. Action: move iso, adjust weighting, check BEV.
"The same hot spot is acceptable inside the PTV and a problem outside it"
10

## Slide 11
02
BLOCK TWO
C
Coverage
⏱ 10 MINUTES
● Volume hierarchy: GTV → CTV → ITV → PTV
● Reading the DVH — V-metrics and D-metrics
● D95, D2, homogeneity index (HI), conformity index (CI)
● Where cold spots live and when they matter
3DCRT Plan Evaluation · Theory Module
11

## Slide 12
BLOCK C · TARGET COVERAGE — DVH & VOLUMES
First: name your volumes
The DVH — your primary instrument
GTV
Gross Tumour Volume — what you can see, palpate or image
CTV
GTV + suspected microscopic spread — the true clinical target
ITV
CTV + internal motion margin (ICRU 62)
PTV
ITV/CTV + set-up uncertainty — the geometric safety margin
We prescribe to and evaluate the PTV — but the clinical aim is to cover the CTV.
Collapses 3-D distribution into one readable curve — every point: what volume gets ≥ this dose?
Read UP from a dose → V-metric (V95, V20 …)
Read ACROSS from a volume → D-metric (D95, D2 … ICRU 83 preferred)
No spatial information — never tells you WHERE the cold or hot spot sits
The DVH screens; the isodose slices diagnose. Always scroll every plane before you trust the DVH.
12

## Slide 13
BLOCK C · COVERAGE METRICS & HOMOGENEITY
The numbers that matter
D95%
Volume of PTV receiving ≥95% of prescription. Standard aim: D95 ≥ 95%.
D2%
Near-maximum — hotspot criterion. ICRU 83: D2% < 107%. Hotspot should sit inside the target.
HI
(D2−D98) ÷ D50. Lower = flatter. < 0.1 good · < 0.15 acceptable.
CI
PIV ÷ TV. Ideal 1.0–1.2. Higher values expected and acceptable in 3DCRT.
Why D98/D2 not Dmin/Dmax? Dmin and Dmax are single-voxel point doses — statistically noisy, shifting with grid size. ICRU 83 replaced them with D98% and D2%: clinically equivalent but stable plan-to-plan.
Coverage is negotiable where PTV abuts a serial OAR — accept a small underdose at the overlap. Safety wins. Know where the cold sits.
13

## Slide 14
03
BLOCK THREE
O
Organs at Risk
⏱ 10 MINUTES
● Serial vs parallel organ architecture
● Matching the right metric: Dmax vs mean vs Vx
● QUANTEC constraints — the working reference
● PRV margins and tolerance negotiation
3DCRT Plan Evaluation · Theory Module
14

## Slide 15
BLOCK O · OAR CONSTRAINTS
Architecture decides the metric — getting this wrong is a class of error
Serial organs
Metric: Dmax or D1cc
One failed sub-unit = organ failure. Even a small dose spike above tolerance causes irreversible damage.
Spinal cord · Brainstem · Optic chiasm · Optic nerves
Apply a PRV margin. Evaluate dose to the PRV, not the bare organ contour.
Cord ≤45 Gy · Brainstem ≤54 Gy · Chiasm ≤54 Gy
Parallel organs
Metric: Mean dose or Vx
Redundant sub-units — organ tolerates partial irradiation. Widespread low dose depletes functional reserve.
Lung · Liver · Kidney · Parotid gland · Bowel
Mean dose predicts function loss; Vx sets the toxicity threshold. Both matter.
Lung V20 <30% · Parotid mean <26 Gy · Rectum V70 <20%
Constraints are not absolutes. Re-irradiation, concurrent chemotherapy, comorbidities, and treatment intent all move the line.
15

## Slide 16
04
BLOCK FOUR
P·S
Prescription & Summation
⏱ 8 MINUTES
● Verifying dose, fractionation and normalisation
● Laterality, intent and plan documentation
● Cumulative dose — or acknowledging none to sum
● Triage: critical, major, minor — and the gut-check
3DCRT Plan Evaluation · Theory Module
16

## Slide 17
P · S — BRINGING IT TOGETHER
Sort every finding into a tier
Your task — the evaluation routine
CRITICAL
Re-plan required — geographic miss · serial OAR above hard limit · hot spot in critical organ
MAJOR
Correct or justify — parallel OAR over constraint · V95 90–95% · avoidable beam through OAR
MINOR
Comment only — slightly high MU · non-ideal isocentre · minor inhomogeneity
Reject on sight if…
1. Cold dose reaching into the CTV · 2. Serial OAR exceeds hard tolerance · 3. Plan is unsafe
Prescription → Contours → Beams → Isodose visual → Coverage → Hotspots → DVH → OARs → Decision
Visual review BEFORE the DVH — scroll every plane first; the DVH cannot tell you WHERE
Name your top 3 concerns before the ideal answer is shown — this separates critical from minor thinking
Fix problems in the right order: contours → geometry → normalisation → optimisation
"Would I confidently treat my own family member with this plan?"
17

## Slide 18
01
CASE 1 · FULL SCORECARD EXERCISE
Whole-Breast Tangents
PRESCRIPTION
2.67 Gy × 15 = 40.05 Gy · Whole breast, right side
TECHNIQUE
3DCRT tangential fields · MLC shaped · possible FiF or wedges
KEY OARS
Heart · Ipsilateral lung · Contralateral breast
5 minutes — score Plan A in the workshop tool. Mark every FCB-CHOPS row before we discuss.
18

## Slide 19
CASE 1 · BREAST · PLAN A · WHAT DO YOU SEE?
[ DVH + Isodose images go here ]
What do you see?
Score every FCB-CHOPS row before we discuss.
Guide your eye to…
Isocentre position — depth, tissue type
Tangent field borders — crossing midline?
Flash beyond breast tissue (≥2 cm?)
Normalisation point location
Hotspot magnitude and location (<115%?)
Heart + lung on DVH
19

## Slide 20
CASE 1 · BREAST · PLAN A — FINDINGS
Plan A is the bad plan
What would have to change?
CRITICAL
Normalisation point in lung — every DVH number is unreliable
CRITICAL
Hotspot >115% — unacceptable magnitude; likely outside PTV
CRITICAL
Heart exceeding tolerance — cardiac dose above constraint
MAJOR
Isocentre too deep — in lung and heart
MAJOR
Fields crossing midline — unnecessary contralateral dose
MAJOR
No flash applied — superficial breast under-coverage
MINOR
No wedges, no dose shaping — but secondary to the above
→ Move isocentre to breast tissue, shallower depth
→ Normalisation point into stable breast tissue
→ Tangent borders must not cross midline
→ Add ≥2 cm flash beyond breast tissue
→ Add wedges or FiF to reduce hotspot <115%
→ Re-check heart and lung on DVH after re-plan
This plan cannot be treated as drawn. The normalisation point failure alone makes every DVH number untrustworthy.
20

## Slide 21
CASE 1 · BREAST · PLANS B & C — ACCEPTABLE → GOOD
Plan B — Acceptable
Wedges
[ Plan B screenshot ]
✓
Good isocentre · norm point in breast · ≥2 cm flash · stays in midline
✓
Hotspot <115% · heart & lung within tolerance
~
HI < 0.15 with wedges — better than Plan A; FiF would improve further
Plan C — Good
Field-in-Field
[ Plan C screenshot ]
✓
Same coverage and OAR sparing as Plan B
✓
Hotspot <110% · HI <0.10 — homogeneous distribution
✓
FiF sub-segments selectively block emerging hot spots
21

## Slide 22
TEACHING MOMENT · CASE 1
Homogeneity — why it matters and how to achieve it
BAD — No shaping
HI > 0.2
No wedges — dose piles up at beam entry. Hotspot is large and often exits the PTV. Normalisation in lung makes all numbers unreliable.
ACCEPTABLE — Wedges
HI < 0.15
Wedge tilts the isodoses to compensate for the sloping breast surface. Hotspot <115%. Clinically deliverable and safe.
GOOD — Field-in-Field
HI < 0.10
FiF sub-segments are forward-planned to block the peak of each hotspot. Same coverage, same OAR sparing — just flatter dose distribution.
22

## Slide 23
02
CASE 2 · GYNAECOLOGY
Whole-Pelvis Irradiation
PRESCRIPTION
1.8 Gy × 25 = 45 Gy · Whole pelvis · cervix + parametria + regional nodes
TECHNIQUE
3DCRT · 4-field box · AP/PA + 2 laterals · FiF applied
KEY OARS
Rectum · Small bowel · Bladder · Femoral heads
Score the plan in the workshop tool. What are your top three concerns?
23

## Slide 24
CASE 2 · GYNAE · WHAT DO YOU SEE?
[ DVH + Isodose images go here ]
What do you see?
Score every FCB-CHOPS row before we discuss.
Guide your eye to…
Does the PTV receive adequate coverage?
Which OARs appear on the DVH — are any lines elevated?
Isodose lines — which normal structures are included?
Rectum: where does the high-dose isodose sit?
Small bowel: any loops visible in the high-dose region?
Bladder + femoral heads within tolerance?
24

## Slide 25
CASE 2 · GYNAE · FINDINGS
✓ Coverage
PTV well covered — target dose maintained throughout
↑ Rectum
V45/V30 elevated — high-dose isodose wraps anterior rectal wall; above QUANTEC tolerance
~ Small bowel
AP/PA component brings anterior bowel into moderate-dose region. V45 elevated.
✓ Bladder
Within acceptable limits
✓ Fem heads
Within tolerance bilaterally
NOTE
Brachytherapy boost to follow — cumulative rectal & bladder dose must be tracked
QUANTEC ref
Rectum: V70 <20%, V50 <50% · 45 Gy whole pelvis: lower-dose constraints apply
25

## Slide 26
CASE 2 · GYNAE · SOLUTIONS
1
Adjust AP/PA vs lateral field weighting to reduce posterior dose to the rectum
2
Patient positioning & preparation — full bladder, belly board, small bowel displacement
3
Reduce posterior PTV margin at the cervix-rectum interface where clearly documented
4
Adjust prescription if clinically appropriate — requires senior discussion
5
Accept with documentation — geometric constraint, not a planning error; record the trade-off explicitly
"EBRT is phase 1. Brachytherapy adds significant rectal and bladder dose. Track cumulative dose from the start."
26

## Slide 27
03
CASE 3 · PROSTATE
Prostate — 3-Field Plan
PRESCRIPTION
2.5 Gy × 27 = 67.5 Gy · Prostate + proximal SVs
TECHNIQUE
AP + 2 posterior obliques · full bladder · empty rectum
KEY OARS
Rectum · Penile bulb · Bladder · Femoral heads · Small bowel
Score the plan in the workshop tool. Which OARs concern you most?
27

## Slide 28
CASE 3 · PROSTATE · WHAT DO YOU SEE?
[ DVH + Isodose images go here ]
What do you see?
Score every FCB-CHOPS row before we discuss.
Guide your eye to…
PTV coverage — D95 and D98 on the DVH
Rectum — where does the curve sit vs tolerance lines?
Penile bulb — is it contoured? What is the mean dose?
Bladder and femoral heads — within tolerance?
Isodose: where does the posterior margin sit relative to the rectum?
Is the isocentre in a stable tissue position?
28

## Slide 29
CASE 3 · PROSTATE · FINDINGS
✓ Coverage
CTV D98 ≈ 99.2% · PTV D98 ≈ 96.6% · Coverage good
↑ Rectum
V55 ≈ 37.9% · V59 ≈ 32.9% — over QUANTEC tolerance
↑ Penile bulb
Mean ≈ 62.8 Gy — above QUANTEC limit of 52 Gy (D90 <50 Gy)
~ Small bowel
Minor focal involvement — within tolerance
✓ Bladder
Within tolerance
✓ Fem heads
Within tolerance
QUANTEC ref
Rectum: V70 <20% V50 <50% · Penile bulb: Dmean <52 Gy D90 <50 Gy
29

## Slide 30
CASE 3 · PROSTATE · SOLUTIONS
1
Reduce inferior field margin — decrease penile bulb dose directly
2
Reduce posterior PTV margin at the prostate–rectum interface
3
Adjust posterior oblique field weighting to shift dose anteriorly
4
Adjust prescription if clinically appropriate — senior discussion required
5
Accept with documentation — geometric proximity, not a planning error; name it, don't ignore it
"Coverage was good — the problem was the OARs. Name it, don't ignore it."
30

## Slide 31
04
CASE 4 · PITUITARY
Pituitary Adenoma — Coplanar 3-Field Plan
PRESCRIPTION
1.8 Gy × 30 = 54 Gy · Pituitary fossa + margin
TECHNIQUE
3-field coplanar · MLC shaped
KEY OARS
Optic chiasm · Optic nerves (bilateral) · Brainstem · Brain
Pay very close attention to the optic chiasm dose.
31

## Slide 32
CASE 4 · PITUITARY · WHAT DO YOU SEE?
[ DVH + Isodose images go here ]
What do you see?
Score every FCB-CHOPS row before we discuss.
Guide your eye to…
D95/D98/Dmin — is the PTV fully covered?
Optic chiasm Dmax — QUANTEC hard limit is 54 Gy
Optic nerves — bilateral Dmax
Brainstem — Dmax and mean dose
Inferior undercoverage — sphenoid sinus physics effect?
Non-coplanar option — does it improve coverage or OAR sparing?
32

## Slide 33
CASE 4 · PITUITARY · FINDINGS
✓ Coverage
PTV D95 adequate
↑ CHIASM
Dmax 54.9 Gy — ABOVE 54 Gy QUANTEC hard limit — mandatory senior sign-off
~ Inferior PTV
PTV min 41.75 Gy — reduced inferior coverage
✓ Brainstem
Dmax 52.5 Gy · Mean ~11 Gy · Within tolerance
NOTE
Sphenoid air sinus undercoverage 88.7% — physics-driven, expected
Architecture
Chiasm is serial: Dmax governs — even small breach = tolerance violation
33

## Slide 34
CASE 4 · PITUITARY — SOLUTIONS: COPLANAR VS NON-COPLANAR
Plan A — Coplanar
Chiasm Dmax: 54.9 Gy ↑ (above tolerance)
PTV min: 41.75 Gy
Brainstem mean: ~11.0 Gy
Plan B — Non-Coplanar
Chiasm Dmax: ~54.9 Gy (SAME — cannot move chiasm)
PTV min: 43.9 Gy (+2.1 Gy improved) ↑
Brainstem mean: 9.7 Gy (↓ 1.6 Gy improved)
"Non-coplanar fields spread entrance angles — but cannot move the chiasm. Documentation required in both plans."
34

## Slide 35
05
CASE 5 · HEAD & NECK
Head & Neck — Parotid Tumour
PRESCRIPTION
2 Gy × 33 = 66 Gy · Parotid tumour + regional nodes
TECHNIQUE
4-field 3DCRT · photon + possible electron match
KEY OARS
Contralateral parotid · Spinal cord · Brainstem · Oral cavity
Focus especially on the contralateral parotid dose.
35

## Slide 36
CASE 5 · H&N · WHAT DO YOU SEE?
[ DVH + Isodose images go here ]
What do you see?
Score every FCB-CHOPS row before we discuss.
Guide your eye to…
PTV coverage — D95, D98
Cord Dmax — hard limit 45 Gy PRV / 50 Gy cord
Brainstem Dmax
Contralateral parotid mean — QUANTEC <26 Gy
Ipsilateral parotid — likely sacrifice; document
Beam entry/exit — does right lateral exit through contralateral parotid?
36

## Slide 37
CASE 5 · H&N · FINDINGS
✓ Coverage
PTV mean ≈ 66.0 Gy — well covered
↑ Contra parotid
Mean ≈ 3.30 Gy — higher than necessary (Plan A, 4-field)
✓ Cord
Dmax 19.9 Gy · Within tolerance
✓ Brainstem
Dmax 18.2 Gy · Within tolerance
~ Submandibular
R mean ≈ 40.4 Gy — elevated
NOTE
Electron/photon match junction — dose at junction must be summed
Cause
Right lateral field exits through contralateral parotid — geometry problem
Late effect
Xerostomia: most common serious late effect of H&N RT — always prioritise sparing
37

## Slide 38
CASE 5 · H&N — SOLUTIONS: 4-FIELD VS 3-FIELD
Plan A — 4-Field
PTV mean: ≈ 66.0 Gy
Contra parotid: 3.30 Gy ↑ (above optimal)
Cord Dmax: 19.9 Gy
Brainstem Dmax: 18.2 Gy
Plan B — 3-Field (right lateral removed)
PTV mean: ≈ 66.0 Gy (maintained)
Contra parotid: 1.14 Gy ↓ (↓ 2.2 Gy improvement)
Cord Dmax: 17.8 Gy (↓ 2.1 Gy)
Brainstem Dmax: 16.1 Gy (↓ 2.1 Gy)
"Fewer fields ≠ worse plan. Remove the beam that exits through the contralateral parotid."
38

## Slide 39
FIVE KEY TAKEAWAYS
1
FCB-CHOPS every time
Use the framework as a safety net — don't skip letters
2
DVH screens; slices diagnose
Use both — DVH flags the problem, isodose slices locate it exactly
3
Match metric to organ architecture
Serial → Dmax / D1cc · Parallel → mean / Vx
4
Normalisation point matters
In lung or air = unreliable; must be in stable representative tissue
5
Document every trade-off
If you accept a compromise, write it down — name it, don't ignore it
References: FCB-CHOPS Weisman 2024 (PMID 40017913) · ICRU 50/62/83 · QUANTEC 2010 · Emami 1991 · Khan textbook
"A good plan is a documented compromise"
39