## Slide 1
RADIATION ONCOLOGY · UCT / GSH REGISTRAR TRAINING
What Makes a Plan Good?
3DCRT Plan Evaluation Workshop · Theory & Practical Module
From bad, to acceptable, to good — a structured approach
Presented by Tamerone Manasse · UCT / GSH Registrars · 2026
FCB-CHOPS
A systematic framework for
every plan evaluation

## Slide 2
HOW THIS SESSION RUNS
Framework, three blocks, a scorecard
BY THE END YOU CAN…
Apply FCB-CHOPS — a complete evaluation checklist
Read a DVH and pull coverage & OAR numbers off it
Explain CI & HI — and what "good enough" means
Apply OAR constraints using serial / parallel logic
Judge technical quality of a 3DCRT plan
Framing & FCB-CHOPS
The central question · framework · your task
0:00 – 0:05
SLIDES 1–6
Block 1 · Target Coverage
Is the right volume getting the right dose?
0:05 – 0:12
SLIDES 7–14
Block 2 · OAR Constraints
Is normal tissue safe — and how do we know?
0:12 – 0:18
SLIDES 15–19
Block 3 · Technical Quality
Is the plan well built and deliverable?
0:18 – 0:23
SLIDES 20–25
Consolidate & Routine
Scorecard tiers · evaluation routine · close
0:23 – 0:25
SLIDES 26–29
3DCRT PLAN EVALUATION
02 / 37

## Slide 3
THE CENTRAL QUESTION
A good plan answers four questions
Run every plan past these four lenses, in order. A plan is never "perfect" — it is the best defensible compromise.
01
Does it treat the target?
Adequate dose to the whole target volume — no geographic miss, no cold spot where tumour lives.
02
Does it spare normal tissue?
Every organ at risk within tolerance — judged against the right dose-volume metric for that organ.
03
Is it technically sound?
Sensible isocentre, beam angles, weighting and shaping — the plan is built, not just generated.
04
Is it deliverable & robust?
Achievable on the machine, and stable to realistic setup and anatomy variation. Undeliverable ≠ good.
3DCRT PLAN EVALUATION
03 / 37

## Slide 4
THE REALITY OF PLAN EVALUATION
Bad, acceptable, trade-off — or good?
Few plans are clearly bad. The hard — and teachable — judgement lives in the middle two categories.
CLEARLY BAD
Unsafe or unacceptable.
Easy to spot, easy to reject.
ACCEPTABLE
Passes constraints — but a
better plan is clearly achievable.
TRADE-OFF
Competing priorities pull against
each other. Needs judgement.
GOOD
Balanced, robust and
clinically appropriate.
THE GUT-CHECK
"Would I confidently treat my own family member with this plan?"
If the answer is not a clear yes — name exactly what would have to change.
3DCRT PLAN EVALUATION
04 / 37

## Slide 5
A SYSTEMATIC FRAMEWORK
FCB-CHOPS — a checklist for every plan
Eight checkpoints so no critical step is missed.
F
Fusion / Imaging
Verify image fusion accuracy to ensure correct target and OAR anatomy.
C
Contours
Check that all target and OAR contours are complete and anatomically correct.
B
Beam Arrangement
Confirm that beam geometry and entry points are appropriate for the target.
C
Coverage
Ensure the prescribed dose adequately covers the target volume.
H
Heterogeneity / Hotspots
Assess internal dose variation for acceptable high and low dose regions.
O
Organs at Risk
Check that OAR doses respect clinical constraints.
P
Prescription
Confirm the correct dose, fractionation, and delivery schedule are used.
S
Summation
Evaluate cumulative dose from all treatment courses / previous RT.
3DCRT PLAN EVALUATION
05 / 37

## Slide 6
A SYSTEMATIC FRAMEWORK
FCB-CHOPS — how to use it
The acronym exists so no critical step is missed — not so you march rigidly from F to S.
HOW TO USE IT
Work in whatever order the plan demands; the letters are a safety net, not a script. The framework is a checklist so that when you look up from the DVH and close the plan, no critical step has been skipped.
START WITH THE PRESCRIPTION
It defines treatment intent, dose, fractionation, technique and priorities. Every downstream judgement flows from it — confirm it before anything else.
THE ORDER IN THIS WORKSHOP
Prescription → Fusion → Contours → Beams → Coverage → Hotspots → OARs → Summation — but always let the plan guide you.
3DCRT PLAN EVALUATION
06 / 37

## Slide 7
01
BLOCK ONE
Target Coverage
10 MINUTES
How to read a dose volume histogram
Coverage metrics — V95, V107, D98, D2, D50
Conformity and homogeneity — and "what is good enough?"
3DCRT PLAN EVALUATION
07 / 37

## Slide 8
BLOCK 1 · TARGET COVERAGE
First, name your volumes
Coverage means nothing until you are clear on which volume you are covering. The ICRU volume hierarchy (Reports 50, 62, 83):
GTV
Gross Tumour Volume
What you can see, palpate or image. No tumour = no GTV.
CTV
Clinical Target Volume
GTV + suspected microscopic spread. The true clinical target.
ITV
Internal Target Volume
CTV + internal motion (e.g. breathing). ICRU 62.
PTV
Planning Target Volume
ITV/CTV + set-up uncertainty. A geometric safety margin.
THE POINT THAT MATTERS FOR EVALUATION
We prescribe to and evaluate dose on the PTV — but the clinical aim is to cover the CTV. A small PTV-edge underdose may still leave the CTV fully covered.
3DCRT PLAN EVALUATION
08 / 37

## Slide 9
BLOCK 1 · TARGET COVERAGE
The DVH — your primary instrument
The cumulative dose–volume histogram collapses a 3-D dose distribution into one readable curve.
Every point answers one question: what volume gets at least this dose?
Read up from a dose → a V-metric
Read across from a volume → a D-metric
Steep target curve = homogeneous full-dose coverage
OAR curve hugging the origin = good sparing
LIMITATION
A DVH has no spatial information. It never tells you WHERE the high or low dose actually sits.
Cumulative DVH — target (blue) and OAR (green)
Volume (%)
Dose (Gy)
100
0
TARGET
curve
OAR
curve
V-metric: read UP →
D-metric: read ACROSS →
3DCRT PLAN EVALUATION
09 / 37

## Slide 10
BLOCK 1 · TARGET COVERAGE
Coverage metrics — the numbers that matter
D95%
(or V95%)
Volume of the PTV receiving ≥95% of the prescribed dose.
Standard aim: D95 ≥ 95% of prescription. Some protocols want ≥98% for the GTV.
D2%
(or V107%)
Near-maximum dose — the hot-spot criterion. Keep the high-dose volume small.
ICRU 83: D2% <107% of prescription dose. Hotspot should ideally sit inside the target.
THE MODERN WAY TO STATE COVERAGE — ICRU 83
ICRU 83 prefers dose-at-a-volume (D95%) over volume-at-a-dose (V95%). Both are in daily use; what matters is that you state which volume and which dose level. "V95" is meaningless until you say V95 of the PTV at the 95% isodose.
3DCRT PLAN EVALUATION
10 / 37

## Slide 11
BLOCK 1 · TARGET COVERAGE
D98 / D2 / D50 — why point doses retired
ICRU 83 replaced Dmin and Dmax with near-min and near-max doses that are clinically equivalent but statistically stable.
D98%
NEAR-MINIMUM
Dose received by 98% of the volume. The robust stand-in for Dmin.
D2%
NEAR-MAXIMUM
Dose received by 2% of the volume. The robust stand-in for Dmax.
D50%
MEDIAN DOSE
Dose to half the volume — the denominator of the homogeneity index.
WHY NOT JUST USE Dmin AND Dmax?
Dmin and Dmax are single-voxel point doses — statistically noisy, shifting with calculation grid size and contouring jitter. ICRU 83 replaced them with D98% and D2%: near-minimum and near-maximum doses that mean almost the same thing clinically but are stable plan-to-plan. Trust a near-max over a Dmax.
3DCRT PLAN EVALUATION
11 / 37

## Slide 12
BLOCK 1 · TARGET COVERAGE
Conformity — is the dose the right shape?
Conformity asks: does the prescription isodose wrap the target — or is it spilling into normal tissue?
Good
Isodose closely follows the target outline on most slices
Marginal
Dose bulges noticeably beyond the target in places; more normal tissue included than needed
Poor
Isodose falls short of the target or misses an edge entirely; target is underdosed
Conformity Index (CI)
CI = PIV / TV (Prescription Isodose Volume ÷ Target Volume)
Ideal: 1.0–1.2. Higher values expected and acceptable in 3DCRT.
3DCRT context
Shaped static beams cannot wrap dose as tightly as VMAT — some bulge is expected and acceptable. Judge against the technique, not an abstract ideal.
3DCRT PLAN EVALUATION
12 / 37

## Slide 13
BLOCK 1 · TARGET COVERAGE
Homogeneity — is the dose evenly spread?
Homogeneity asks whether dose is uniform across the target — no hot core, no cold shoulders.
HI = (D2% − D98%) ÷ D50%
Lower is flatter — ICRU 83; ideal near 0, <0.1 good, <0.15 acceptable
Hot spots → normal-tissue toxicity beyond the target
Cold spots → risk of local recurrence within the target
3DCRT tools — wedges, field-in-field (FiF), compensators
Note: SBRT
SBRT deliberately runs inhomogeneous — a hot core is intended. HI thresholds apply to conventional fractionation only.
3DCRT PLAN EVALUATION
13 / 37

## Slide 14
BLOCK 1 · TARGET COVERAGE
"What is good enough?"
Coverage numbers are not pass/fail laws. They are negotiated — against OAR safety, intent and what the technique can deliver.
Coverage is negotiable
Where the PTV abuts a serial OAR, you accept a small underdose at the overlap rather than breach a hard tolerance. Safety wins.
Know where the cold sits
Underdose at the PTV margin may leave the CTV intact. Underdose reaching into the CTV is a different, serious problem.
Intent sets the bar
Radical treatment demands tighter coverage than palliation. "Good enough" for pain relief is not "good enough" for cure.
Achievable, not ideal
Judge against what 3DCRT can realistically deliver for this anatomy — not against an inverse-planned VMAT distribution.
3DCRT PLAN EVALUATION
14 / 37

## Slide 15
02
BLOCK TWO
OAR Constraints
10 MINUTES
Serial vs parallel organs — architecture decides the metric
Tolerance doses, QUANTEC and dose–response
Clinical context, modifiers and the PRV
3DCRT PLAN EVALUATION
15 / 37

## Slide 16
BLOCK 2 · OAR CONSTRAINTS
Serial vs parallel — architecture sets the rule
How an organ is structured decides which metric matters. Getting this wrong is a class of error.
SERIAL
One failed sub-unit = organ failure
Governed by: Dmax or D1cc
Examples: Spinal cord · Brainstem · Optic chiasm · Optic nerves
Risk: Even a small dose spike above tolerance causes irreversible damage
PRV: Apply a margin — evaluate dose to the PRV, not the bare organ
PARALLEL
Redundant sub-units — organ tolerates partial irradiation
Governed by: Mean dose or Vx Gy
Examples: Lung · Liver · Kidney · Parotid gland
Risk: Widespread low-dose irradiation depletes functional reserve
Key metric: Mean dose predicts loss of function; Vx sets threshold for toxicity
3DCRT PLAN EVALUATION
16 / 37

## Slide 17
BLOCK 2 · OAR CONSTRAINTS
Tolerance doses — where the limits come from
Emami
1991
First systematic tolerance table — TD5/5 and TD50/5. Largely expert consensus. Now largely superseded but still referenced.
QUANTEC
2010
Evidence-based organ-by-organ dose–volume limits with defined endpoints. The working reference for conventional fractionation.
Protocol sets
RTOG/NRG
Site-specific, trial-vetted constraints. HyTEC for hypofractionation and SBRT. Always plan to the named protocol.
THE CAVEAT THAT MATTERS
Most QUANTEC data come from conventionally fractionated 3DCRT (~1.8–2 Gy per fraction). Change the fractionation and you must think in BED / EQD₂ — never read a 2 Gy/fraction number straight onto an SBRT plan.
3DCRT PLAN EVALUATION
17 / 37

## Slide 18
BLOCK 2 · OAR CONSTRAINTS
Match the metric to the organ
Read the constraint, identify the organ type, then pull the matching number off the DVH. Mismatched metrics are a classic error.
Dmax / near-max
SERIAL
Serial organs — spinal cord, brainstem, optic chiasm & nerves
Mean dose
PARALLEL
Parallel organs — parotid (xerostomia), lung (pneumonitis), liver, kidney
Volume at a dose
PARALLEL
Threshold/mixed organs — lung V20, rectum V70 & V50, heart V25
Dose to a sub-volume
MIXED
Dx cc — near-max to a small absolute volume; robust for serial structures
3DCRT PLAN EVALUATION
18 / 37

## Slide 19
BLOCK 2 · OAR CONSTRAINTS
Constraints are not absolutes — context shifts them
→
Re-irradiation
Prior dose has spent part of the tolerance budget. Some organs recover partially over time — but stay conservative.
→
Concurrent systemic therapy
Chemo lowers tolerance — e.g. cisplatin + cochlea, several agents + lung. The constraint tightens.
→
Patient factors
Age, smoking, diabetes, connective-tissue disease, prior surgery and baseline organ function all move the line.
→
Treatment intent
Radical treatment justifies accepting more risk than palliation. The acceptable trade-off depends on the goal.
THE PRV · Planning organ-at-risk volume — a margin grown around a serial OAR for set-up and motion uncertainty. Evaluate dose to the PRV, not the bare organ.
3DCRT PLAN EVALUATION
19 / 37

## Slide 20
03
BLOCK THREE
Technical Quality
10 MINUTES
Isocentre, beam angles and field arrangement
Beam weighting, wedges, collimation and MLC shaping
Hot spots, dose gradient and integral dose
3DCRT PLAN EVALUATION
20 / 37

## Slide 21
BLOCK 3 · TECHNICAL QUALITY
Technical quality — what to evaluate
Here the question shifts: not 'how does it work' but 'is it used well in this plan?'
ISOCENTRE
Centred in the PTV — balances field sizes, keeps the target away from field edges
Not in lung or at a density interface — dosimetrically unstable positions
Beam angles — converge on the target, avoid transiting through OARs
Wedges / FiF — applied where the contour slopes or hot spots emerge
COLLIMATION & SHAPING
MLC conforms to PTV BEV — with a real penumbra margin, not clipped tight to the PTV
Hot spot location — 107% inside the PTV is fine; in skin or an OAR it is not
Monitor units — sanity-check; excess MU adds scatter and integral dose
Normalisation — prescription point in stable, representative tissue
3DCRT PLAN EVALUATION
21 / 37

## Slide 22
BLOCK 3 · TECHNICAL QUALITY
Technical red flags — patterns that signal a problem
Spot one of these — name it, explain the risk, say how to fix it.
Isocentre in lung, air, or at a tissue interface
Risk: Dosimetrically unstable — dose calculations unreliable
Fix: Move isocentre into the target or stable tissue
A beam transiting directly through a critical OAR
Risk: Unnecessary dose to serial organ — myelopathy, blindness, necrosis risk
Fix: Re-angle the beam if any workable alternative solves it
Hot spot outside the PTV
Risk: High dose in skin, bowel, or OAR is unacceptable regardless of magnitude
Fix: Adjust weighting, add a field or FiF sub-segment
MLC clipped tight to the PTV
Risk: No penumbra margin — cold rim on every beam; guaranteed underdosage
Fix: Open MLC to leave a 3–5 mm penumbra margin beyond the BEV PTV
3DCRT PLAN EVALUATION
22 / 37

## Slide 23
BLOCK 3 · TECHNICAL QUALITY
Shaping the dose — weighting, wedges, modulation
Beam weighting
The relative dose contribution of each field. Re-weight to pull the hot spot into the target and balance dose — e.g. AP/PA vs the laterals.
Wedges
Physical or dynamic. Tilt the isodoses to compensate for a sloping surface or missing tissue — the classic use is breast tangents.
Field-in-field (FiF)
Forward-planned sub-segments that block emerging hot spots. The modern 3DCRT homogenisation tool — routine in breast.
Compensators
Physical compensators or bolus to manage missing tissue and surface dose where wedges or segments are not enough.
3DCRT PLAN EVALUATION
23 / 37

## Slide 24
BLOCK 3 · TECHNICAL QUALITY
Collimation & MLC shaping
The MLC and collimator shape each field to the beam's-eye-view of the target. Conform tightly — but never clip the PTV.
●
MLC conformance
Shape the field to the BEV of the PTV plus a penumbra margin. Too tight clips the target; too loose wastes normal tissue.
●
Collimator rotation
Rotate to match the field shape to the PTV, minimise the MLC 'staircase', and manage divergence at field junctions.
●
Penumbra margin
The MLC leaf edge is not the dose edge. Leave margin so the PTV sits inside the high-dose region, not in the falloff.
●
Tongue-and-groove
Slight underdose along leaf sides. Minimised by sensible collimator-angle choice — know it exists.
3DCRT PLAN EVALUATION
24 / 37

## Slide 25
BLOCK 3 · TECHNICAL QUALITY
Hot spots, dose gradient & integral dose
Three final technical reads — and the first one is the most-missed.
Hot spot — location, not just size
D2% <107% inside the PTV is fine; in skin or an OAR it is not. Location is the primary concern.
Dose gradient
Dose should fall steeply between the PTV and any adjacent OAR. A shallow gradient = unnecessary OAR exposure.
Integral dose / MU
Sanity-check the monitor units. Excess MU adds scatter and integral dose — the whole patient receives more radiation.
The same hot spot is acceptable inside the PTV and a problem outside it — always check where, not just what.
3DCRT PLAN EVALUATION
25 / 37

## Slide 26
BRINGING IT TOGETHER
The scorecard, revisited
You now have the concepts. Sort them into the three tiers — that sorting is the clinical skill.
CRITICAL
Plan fails — re-plan
Geographic miss of the target · serial OAR over a hard tolerance · hot spot in a critical organ.
MAJOR
Correct it or justify it
Parallel-OAR mean over constraint · coverage V95 90–95% · a beam through an avoidable OAR.
MINOR
Comment — rarely decisive
Slightly high MU · minor inhomogeneity · a non-ideal but workable isocentre.
REJECT ON SIGHT IF…
1
Cold dose reaching into the CTV — not just the PTV margin
2
A critical serial organ exceeds a hard tolerance — cord, brainstem, chiasm
3
The plan is unsafe or undeliverable as drawn
3DCRT PLAN EVALUATION
26 / 37

## Slide 27
PUTTING IT TO WORK
A repeatable evaluation routine
Same sequence, every plan, every time — then the handful of habits that catch the errors checklists miss.
1
Prescription
2
Contours
3
Beam arrangement
4
Isodose — visual
5
Coverage
6
Hot / cold spots
7
DVH
8
Organs at risk
9
Final clinical decision
Visual review before the DVH
Scroll the isodoses on every plane first — the DVH cannot tell you WHERE.
The DVH confirms, never replaces
Use it to verify what the images already showed you — not instead of them.
Fix problems in the right order
Contours → geometry → normalisation → optimisation → fine-tune. Never start with objectives.
Robustness, not perfection
Ask what happens if the patient shifts or the bladder fills — a slightly less perfect plan can be safer.
3DCRT PLAN EVALUATION
27 / 37

## Slide 28
WRAP-UP
Key takeaways & references
A good plan is a documented compromise
Target covered, OARs within tolerance, technically sound, deliverable — and every trade-off articulated.
The DVH screens; the slices diagnose
It has no spatial information. Always confirm where the cold and hot regions actually sit.
Match the metric to the organ
Architecture — serial or parallel — decides whether you read Dmax or mean dose.
Prioritise — not every deviation is equal
Three reject-on-sight failures; everything else is graded, justified discussion.
REFERENCES
FCB-CHOPS — Weisman et al., Adv Radiat Oncol, 2024
ICRU Reports 50, 62 & 83 · QUANTEC — IJROBP 2010;76(3) Suppl · Emami et al. 1991 · HyTEC · Khan, Treatment Planning in Radiation Oncology
3DCRT PLAN EVALUATION
28 / 37

## Slide 29
YOUR TASK TODAY
Complete the score card as you review each plan
The skill we are training is triage — the score card tool structures your thinking so the case review is richer.
CRITICAL
Reject
Unsafe dose or missed target.
Needs re-plan.
MARGINAL
Comment
Acceptable but improvable.
Flag and discuss.
PASS
Approve
Meets all criteria.
Record and move on.
IN THE SCORE CARD TOOL
Score each parameter: Pass / Marginal / Fail — and add a free-text note for each finding. Your completed scorecard will anchor the case review discussion that follows.
BEFORE CASE REVIEW
"What are your top three concerns with this plan?"
Name your top three concerns before the ideal answer is shown — this separates critical from minor thinking.
3DCRT PLAN EVALUATION
29 / 37

## Slide 30
04
BLOCK FOUR
Case Reviews
90 MINUTES
1
Case 1: Breast (3 plans)
2
Case 2: Gynae — Trade-off
3
Case 3: Prostate — Trade-off
4
Case 4: Neuro — Pituitary (2 plans)
5
Case 5: H&N — Parotid (2 plans)
3DCRT PLAN EVALUATION
30 / 37

## Slide 31
BLOCK 4 · CASE REVIEWS
Case 1: Breast
BAD PLAN
No Wedges
Poor iso placement (too deep into lung & heart)
Crossing midline — unnecessary contralateral dose
No flash applied — under-coverage of superficial breast
Poor normalisation point placement (in lung)
Unacceptable hotspot (>115%) and location
No dose shaping; poor homogeneity
Heart exceeding tolerance
ACCEPTABLE
Wedged
Good iso placement
In midline — contralateral spared
Flash applied (≥2 cm beyond breast tissue)
Good normalisation point; good coverage
Acceptable hotspot (<115%) and location
Wedges applied — improved homogeneity
Heart & lung within tolerance
GOOD PLAN
FiF
Good iso placement
In midline — contralateral spared
Flash applied (≥2 cm beyond breast tissue)
Good normalisation point; good coverage
Acceptable hotspot (<110%) and location
FiF — selective reduction of hotspots using subfields
Heart & lung within tolerance
3DCRT PLAN EVALUATION
31 / 37

## Slide 32
BLOCK 4 · CASE REVIEWS
Case 2: Gynaecology
TRADE-OFF PLAN
4-Field Box (FiF)
PTV coverage → ✓ good and maintained
Rectum dose → ↑ exceeds tolerance (e.g. V45 / V30)
High dose region extends into posterior pelvis (rectum region)
Dose distribution driven by anterior–posterior beam contribution
Other OARs (bladder, bowel) → ✓ within acceptable limits
Improving rectum dose would compromise target coverage
Current plan prioritises coverage over rectum sparing
No clear way to improve both without introducing a compromise
Discussion: Is this a clinically acceptable trade-off? What would you change, and what would you sacrifice?
3DCRT PLAN EVALUATION
32 / 37

## Slide 33
BLOCK 4 · CASE REVIEWS
Case 3: Prostate
TRADE-OFF PLAN
3-Field
PTV coverage → ✓ good (CTV D98 ≈ 99.2%, PTV D98 ≈ 96.6%)
Rectum → ↑ exceeds tolerance (V55 ≈ 37.9%, V59 ≈ 32.9%)
Penile bulb mean ≈ 62.8 Gy → ↑ significantly above tolerance
Small bowel → ✓ mostly within limits, minor focal exceedance (V52)
Bladder → ✓ well controlled and within all constraints
Femoral heads → ✓ within tolerance
Reducing rectum / penile bulb dose would compromise target coverage
Plan prioritises coverage — requires clinical decision, not simple optimisation
Discussion: Rectum V55 and penile bulb are both above tolerance. What is the clinical priority? Accept, modify, or escalate?
3DCRT PLAN EVALUATION
33 / 37

## Slide 34
BLOCK 4 · CASE REVIEWS
Case 4: Neuro — Pituitary Adenoma
ACCEPTABLE
Coplanar
PTV min = 41.75 Gy → inferior coverage reduced
Optic chiasm max = 54.9 Gy → high but acceptable
Optic nerves ~53 Gy max → reasonable
Brainstem max = 52.5 Gy, mean ~11 Gy → acceptable
Air region undercoverage (88.7%) → physics-driven
No major planning errors — clinically deliverable
Improvement achievable with non-coplanar arrangement
GOOD PLAN
Non-Coplanar
PTV min = ~43.9 Gy → improved inferior coverage (↑~2.1 Gy)
Optic chiasm max ≈ 54.9 Gy → similar, no meaningful change
Optic nerves → similar; R nerve mean ↓~2 Gy (slight improvement)
Brainstem max ≈ 52.1 Gy, mean ~9.7 Gy → mean ↓~1.6 Gy
Air region undercoverage (~88.7%) → unchanged, physics-driven
Optimal use of geometry to manage anatomical limitation
Improvements achieved without compromising other structures
Key teaching: optic chiasm at 54.9 Gy — marginal. Explicit clinical justification must be documented.
3DCRT PLAN EVALUATION
34 / 37

## Slide 35
BLOCK 4 · CASE REVIEWS
Case 4 Teaching Points — Pituitary Adenoma
Why the pituitary fossa makes optic structure dose a central planning challenge.
Proximity to optic structures
The pituitary fossa sits immediately below the optic chiasm — PTV and chiasm are often adjacent or overlapping. This makes coverage vs chiasm sparing an intrinsic geometric tension.
Chiasm tolerance: 54 Gy hard limit
Optic chiasm Dmax <54 Gy (QUANTEC). This plan: 54.9 Gy — marginal. Explicit clinical justification and documentation required. Any breach requires senior discussion.
Non-coplanar fields — why they help
Non-coplanar beams spread dose across more of the skull base, reducing the dose contribution from any one direction and improving inferior PTV coverage without worsening OAR dose.
Air cavity undercoverage
Sphenoid air sinus undercoverage (88.7%) is physics-driven — air has near-zero electron density. This is expected and should be documented, not corrected by over-dosing adjacent structures.
3DCRT PLAN EVALUATION
35 / 37

## Slide 36
BLOCK 4 · CASE REVIEWS
Case 5: H&N — Parotid Tumour
ACCEPTABLE
4-Field Plan
Target coverage (PTV High) mean ≈ 66.0 Gy → ✓ acceptable
Contralateral parotid (L) mean ≈ 3.30 Gy → ↑ higher dose (less sparing)
Spinal cord max ≈ 19.9 Gy → ✓ within tolerance
Brainstem max ≈ 18.2 Gy → ✓ within tolerance
Oral cavity mean ≈ 17.2 Gy → ✓ similar
Submandibular gland (R) mean ≈ 40.4 Gy → ↑ higher dose
No major planning errors — clinically deliverable
Improvement achievable with 3-field arrangement
GOOD PLAN
3-Field Plan
Target coverage (PTV High) mean ≈ 66.0 Gy → ✓ maintained
Contralateral parotid (L) mean ≈ 1.14 Gy → ↓ improved (~2.2 Gy reduction)
Spinal cord max ≈ 17.8 Gy → ↓ lower (~2 Gy reduction)
Brainstem max ≈ 16.1 Gy → ↓ lower (~2 Gy reduction)
Oral cavity mean ≈ 17.2 Gy → ✓ similar
Submandibular gland (R) mean ≈ 40.0 Gy → ↓ slight improvement
Optimal use of geometry to manage anatomical limitation
Improvements achieved without compromising other structures
Key teaching: fewer fields can mean better sparing — reducing beams through the contralateral side dramatically reduces parotid and cord dose.
3DCRT PLAN EVALUATION
36 / 37

## Slide 37
BLOCK 4 · CASE REVIEWS
Case 5 Teaching Points — Parotid Tumour
Why parotid cases are a masterclass in balancing coverage and contralateral xerostomia.
Contralateral parotid sparing
The contralateral parotid mean <26 Gy target (QUANTEC) is critical for xerostomia prevention. The 3-field plan achieves 1.14 Gy vs 3.30 Gy — a clinically significant difference in long-term QoL.
Fewer fields can mean better sparing
The 4-field plan routes beams through the contralateral side. Removing those fields — if target coverage is maintained — is the single most effective change for xerostomia. Don't default to more fields.
Target coverage maintained in both
Both plans achieve comparable primary PTV mean dose (~66 Gy). The improvement in the 3-field plan is entirely in OAR sparing — not at the cost of coverage.
Spinal cord and brainstem also improve
The 3-field plan also reduces cord max (19.9 → 17.8 Gy) and brainstem max (18.2 → 16.1 Gy). Serial organ dose reduction is a secondary benefit of the geometry change.
3DCRT PLAN EVALUATION
37 / 37